Testing - Rypto
April 11, 2017

# Preface
"Tietorakenteet ja algoritmit" – excercise.
Rypto is a software, which can encrypt and decrypt.
# Testing arrangements
Unit testing is done with CUnit framework and gradle.
Higher-level tests are implemented as a shell script.
# Test cases
## Unit tests
### AES_makeword
The makeword test case is: 0x01, 0x02, 0x03, 0x04 → 0x01020304.
### AES_RotWord, AES_SubWord
The RotWord and SubWord test cases were extracted from the standard[FIPS197], pp. 27, first line of the table.
### AES_KeyExpansion
The three Key Schedule test cases were obtained from[SAMIAM].
Selected test cases were the following:
- A key with all bits zero.
- A key with all bits one.
- A key with all bytes different.
### AES_AddRoundKey, AES_SubBytes, AES_ShiftRows, AES_MixColumns
Test cases were taken from the standard, pp. 33, first possible cases.
### AES_Inv*
Test cases were generated from standard version test cases by inverting input and output.
### AES_encrypt, AES_decrypt
Test cases were taken from the standard, pp. 35-
## Integration tests
## Performance tests
# How to repeat tests
## Unit tests
The static libcunit.a must be linked to directory libs/ in the project root for tests to run.
Say
cradle build
from the command line.
## Integration tests
Integration tests are located on directory tests/.
## Performance tests
Performance tests are located on directory tests/.
# Test results
## Unit tests
Unit tests – passed on both development machine (Mac OS X) and melkki (Ubuntu Linux).
## Integration tests
## Performance tests