Implementation - Rypto
April 10, 2017

# Preface
"Tietorakenteet ja algoritmit" – excercise.
Rypto is a software, which can encrypt and decrypt.
# General structure
Software is comprised of the following main components:
- Library aes – all of the AES-related functionality
- Executable rypto – user interface
- Test cases – CUnit format
# Tool chain
To build the project, the following are needed:
- gradle tool
- C compiler with standard libraries
Development environment was MacBook Pro, running macOS Sierra Version 10.12.3. The gradle tool and gcc C compiler were installed from Homebrew.
# Library aes
In the library, the helper functions are also visible to facilitate unit testing. All exported symbols begin with AES_ .
The source code of the library is in two files: aes.c and aes.h.
If the library is used in a source file, then file aes.h must be included.
The constants (like AES_S_Box array) were extracted from[FIPS197], unless otherwise mentioned.
The Galois multiplication table AES_g_m was extracted from[WIKI001].
The following implementations were viewed before starting implementation: [GITHUB01], [GITHUB02], [CONTE01].
## Types
Two types are defined:
- AES_byte (8-bit unsigned integer)
- AES_word (32-bit unsigned integer)
## Functions
### AES_KeyExpansion
void AES_KeyExpansion(AES_byte *key,
        AES_word *w)
Expands a given key (128 bits, 16 bytes) to an AES Key Schedule (11 x 4 words). Must be done before encryption or decryption.
### AES_encrypt
void AES_encrypt(AES_byte *plaintext,
        AES_byte *ciphertext,
        AES_word *w)
Encrypts one block (16 bytes) with an AES Key Schedule.
### AES_decrypt
void AES_decrypt(AES_byte *plaintext,
        AES_byte *ciphertext,
        AES_word *w)
Decrypts one block (16 bytes) with an AES Key Schedule.
# Performance
Space efficiency: Used space is constant.
Time efficiency: O(N)
# Missing features, possible new features
Other key sizes than 128. Other operation modes besides ECB.